## Slide 1: Computer System Servicing

## Slide 2: RECALL/RECAP

## Slide 3
Motivation:

## Slide 4: Creating Crossover Cable

## Slide 5: Crossover Cable
A type of cable used for the interconnection of two similar devices.

## Slide 6: Steps in Creating Crossover Cable
1. Prepare the tools and materials.

## Slide 7: Steps in Creating Crossover Cable
2. Cut the twisted-pair cable based on the needed length.

## Slide 8: Steps in Creating Crossover Cable
3. Remove the outer jacket of the cable to expose the four pairs of wire inside.

## Slide 9: Steps in Creating Crossover Cable
4. Untwist the wires, make sure that they are free from any damage.

## Slide 10: Steps in Creating Crossover Cable
5. Arrange the wire based on the type of cable.

## Slide 11: Steps in Creating Crossover Cable
5. Arrange the wire based on the type of cable.

## Slide 12: T568-A

## Slide 13: T568-B

## Slide 14: Steps in Creating Crossover Cable
6. Cut the wires so that they will be of exact length, make sure that the ends of the wires are aligned.

## Slide 15: Steps in Creating Crossover Cable
7. Firmly hold the cable and insert the wires into the RJ45 jack.

## Slide 16: Steps in Creating Crossover Cable
8. Check if the end of the wires touches the end of the RJ45 jack.

## Slide 17: Steps in Creating Crossover Cable
9. Plug the cable into the crimping tool, firmly squeeze it while securely holding the cable.

## Slide 18: Steps in Creating Crossover Cable
10. Use a LAN Tester to ensure that the connection of all wires in both ends of the cable.

## Slide 19
FORMATIVE ASSESSMENT
Direction: Arrange the following sequence of steps in creating straight-through cable.
Write numbers 1-10 on the blank line.

## Slide 20
FORMATIVE ASSESSMENT
__ Use a LAN tester to ensure that the connection of all wires in both ends of the cable.
__ Prepare the tools and materials.
__ Plug the cable into the crimping tool, firmly squeeze it while securely holding the cable.
__ Cut the twisted-pair cable based on the needed length.
__ Check if the end of the wires touches the end of the RJ45 jack.
__ Remove the outer jacket of the cable to expose the four pairs of wires inside.
__ Firmly hold the cable and insert the wires into the RJ45 jack.
__ Untwist the wires, make sure that they are free from any damage.
__ Cut the wires so that they will be of exact length, make sure that the ends of the wires are aligned.
__ Arrange the wires based on the type of cable.

## Slide 21
Practical Application of the acquired
Learning Competencies

## Slide 22
GENERALIZATION

## Slide 23
THANK YOU!!!